GENERAL

- Refer to the service manual for the engine model on which you will be testing.

- Make sure the vehicle’s battery is at or near full charge.

PREPARATION

- Remove the glow plug from the cylinder being tested.

- Shut off fuel supply at source.

- Turn the engine over for a few revolutions to blow out any carbon or foreign matter from the port area.  Take special care to prevent dirt, parts and tools from falling into an open glow plug port.

- Screw the adapter firmly into the glow plug hole.  Do not over tighten.

- Attach female quick coupler end on the Hose and Gage Assembly to the male end of the adapter.  Make sure coupler is fully engaged on adapter.

COMPRESSION TEST

- Crank the engine at least 5 engine cycles to achieve highest cylinder pressure.

- Gage reading may be brought back to zero by depressing relief valve located on hexagonal fitting attached to gage.

- Depress the gage relief valve to reset the gage to the zero position.

- Additional tests can be made on each cylinder in the same manner.

# Text boxes

INSTRUCTIONS

DIESEL COMPRESSION TESTER

ADAPTER

8mm KUBOTA

Ver. 52316