GENERAL

- Refer to the service manual for the engine model on which you will be testing.

- Make sure the vehicle’s battery is at or near full charge.

PREPARATION

- Shut off fuel supply at source.

- Remove the fuel injector from the cylinder being tested.

- Turn the engine over for a few revolutions to blow out any carbon or foreign matter from the port area.

- Take special care to prevent dirt, parts and tools from falling into an open injector hole.

- Make sure nylon washer is properly seated at end of end adapter.

- Place adapter into injector hole, place clamp on top of injector and tighten with bolts from removed injector.  Do not over tighten.

- Attach female quick coupler end on the Hose and Gage Assembly to the male end of the adapter.  Make sure coupler is fully engaged on adapter.

COMPRESSION TEST

- Crank the engine until maximum pressure is reached – usually with 8-12 cycles.

- Gage reading may be brought back to zero by depressing relief valve located on hexagonal fitting attached to gage.

- Depress the gage relief valve to reset the gage to the zero position.

- Additional tests can be made on each cylinder in the same manner.

81606

# Text boxes

INSTRUCTIONS

DIESEL COMPRESSION TESTER

ADAPTER FOR 5.9L CUMMINS 24 VALVE ELECTRONIC AND 5.9L ISB, ISBE, ISC & QSB ENGINES

(Nylon Washer

Adapter(

Clamp(