GENERAL

- Refer to the service manual for the engine model on which you will be working.

- Make sure the vehicle’s battery is at or near full charge.  It may be necessary to hook up a battery charger to perform the test.

- Make sure the oil in the crankcase is of the correct viscosity and at the correct level.

PREPARATION

- Operate the engine unit it is at its normal operating temperature.

- Shut off fuel supply at source.

- Remove all glow plugs to check any cylinder.

- Take extra care to prevent parts, debris, or tools form falling into an open glow plug port.

- Thread test adapter into the glow plug port of the cylinder to be tested.  Hand tighten only.

- Attach the test gage hose to the end of the adapter.

COMPRESSION TEST

- Make sure the ignition switch is in the off position.

- Set the throttle plates to the wide open position.

- Crank the engine a minimum of 5 compression strokes and record the highest reading.

- Repeat the procedure for the rest of the cylinders.

- The lowest reading should be within 75% of the highest reading.

# Text boxes

INSTRUCTIONS

DIESEL COMPRESSION TESTER ADAPTER

FOR

FORD 6.0L

Form 41107